## Slide 1
Respects The Globe, Respected Globally
Body Liner Counting @ Thermoforming Machine No#3
14th - 21st Nov 2023
Project Performed by: Abu Bakr Siddique

## Slide 2
Hardware Overview
12V, 5A Power Supply
12V, 0.7A
AC-DC Buck Regulator
LM2596 – 12 to 5V Regulator
LM2596 – 12 to 5V Regulator
AMS1117 – 5V to 3.3V regulator
ESP32 DEVKIT DOIT V1
List of Items:
12V, 5A Power Supply: x1
LM2596: x2
ESP32DEVKIT DOIT V1: x1
12V AC-DC Buck Regulator: x1
AMS1117: x2
Veroboard/ StripBoard: x2
Wires

## Slide 3
Flowchart

## Slide 4
Pipeline Overview
End-to-End IoT Data Pipeline – ESP32, Google Sheets, IFTTT and AppScript
4
3
1
2
Google AppScript
Connect to Wi-Fi
Trigger the Webhook, to send JSON data* to Google Sheets.
Send the JSON data* to store it in Google Sheets
Request to read the data from Google Sheets
AppScript sends the requested data to ESP32
5
6
Send Hourly Email
*Note: JSON Data contains – hourly Liner Counts, Total Liner Counts, Total Liner Counts Saved in previous hour, Today’s date and Last Uploaded Hour

## Slide 5
Field-Test Results
Chart: Auto Vs Manual Counts % Diff. over few days
| 14th Nov | 15th Nov | 18th Nov
Series 1 | -59.1 | -16.4 | 0
Pitfalls & Potential Problems:
Occasional Internet Connectivity
Test Runs = Additional SFG* Counts
V1 (-59.1%)
V2 (-16.4%)
V3 (0%) – may vary by 1 or 2 liners maximum
*Note: SFG – Semi Finished Goods. They are the outcomes or individual products from each section of the factory e.g. Body Liners (FF and FRZ) or Door Liners (Upper and Lower Door) are SFG of Thermoforming.

## Slide 6
Output Overview

## Slide 7
Further Development
Dashboard Containing all the data
Dashboard
Model-Based Counting System
Wastage Counting System
Collection of Data for Big Data Analytics
Avoid Counting Test Runs